## Slide 1
TOPIK 7 — INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
PROGRES MINGGU INI: PERANCANGAN ARSITEKTUR HARDWARE
CONCLUSION SUPPLY CHAIN CONSULTANT:
• 1. Zulfikar Jafarudin Fatah (24D507001001) — Lead System Architect (Ketua Tim) • 2. Armansyah Muchtarrom (24D507001010) — Hardware & Infrastructure Specialist (Presenter) • 3. Afriansayah Ayubi (24D507001026) — Software & ERP Process Specialist • 4. Juan Gamaliel (24D507001016) — Data Integration Specialist • 5. Naufal Andika Heditya (24D507001012) — Business Analyst & QA Specialist
Mata Kuliah: Teknologi dan Perangkat Lunak Logistik • Dosen Pengampu: Dr. Tigor Franky, S.T., M.T.
Program Studi Manajemen Logistik • Institut Transportasi dan Logistik (ITL) Trisakti • September 2026

## Slide 2
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Lanskap Ekosistem Hardware: 6 Klaster Operasional Terminal 35 Ha
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 2 of 15
TANTANGAN FISIK LAPANGAN
Standar Maritim & Heavy-Duty
• Luas area 35 Ha dengan manuver rutin truk trailer 40ft & Reach Stacker 45 ton. • Operasi 24/7 non-stop di bawah terik matahari, debu semen/kontainer, & kelembapan tinggi. • Kebutuhan Proteksi Industri: - Bodi tahan cuaca & air: IP67 / IP68. - Komputer tanpa kipas (Fanless Industrial PC). - Tahan getaran guncangan: MIL-STD-810G. - Standar keselamatan rel KA: SIL 4.
SEBARAN 26 HARDWARE
6 Klaster Kritis Lapangan
1. Otomasi Gate (8 Item): ANPR, OCR, Timbangan 80t, RFID, Barrier, LED, Edge PC. 2. Yard & Alat Angkat (4 Item): DGPS RTK, Twistlock Spreader, VMT, Rugged PDA. 3. Cold Chain (2 Item): Smart Socket 380V & Thermal Camera. 4. Rail Siding (3 Item): Axle Counter, AP WiFi 7, GPS Truk. 5. Bea Cukai (5 Item): Gantry X-Ray 6 MeV, Smart E-Seal, CCTV. 6. Core IT (4 Item): Datacenter, Switch PoE+, Online UPS.
STRATEGI KONSULTAN
Rasionalisasi Menuju Slide 3
• Tidak Semua Hardware Bekerja Sama: - Ada perangkat aktif penghasil data transaksi telemetri dinamis. - Ada perangkat infrastruktur pasif sebagai pendukung fasilitas fisik. • Efisiensi Anggaran (CAPEX Rp 18,94 M): Pengadaan dirancang berbasis prioritas otomasi & kepatuhan regulasi. • Jembatan Implementasi: Diperlukan pemisahan tegas antara hardware yang disimulasikan alur datanya vs hardware blueprint fisik.

## Slide 3
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Strategi Klasifikasi: 11 Perangkat Simulasi vs 15 Perangkat Blueprint
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 3 of 15
11 PERANGKAT SIMULASI (LIVE SOFTWARE & POSTMAN)
Perangkat Aktif Penghasil Aliran Data Telemetri Dinamis
1. Kamera ANPR Gate (Hikvision DS-TCG406-E) — Plat Truk 2. Kamera OCR Portal (Hikvision iDS-TCV300) — Nomor ISO 6346 6. Jembatan Timbang 80t (Fangda Scale) — Validasi SOLAS VGM 7. RFID Reader UHF 20m — Identifikasi e-Pass Supir 10. LED Display Gerbang — Panduan Blok Yard Sopir 18. Industrial Edge AI PC (Advantech ARK-3532) — Gateway JSON 21. DGPS / RTK GNSS (<2 cm) — Auto Bay-Row-Tier 22. Spreader Twistlock & Load Cell — Konfirmasi Lift-Off / Lo-Lo 23. Smart Reefer Socket 380V — Monitoring Daya kWh & Trip 25. Rail Axle Counter (Frauscher) — Hitung Gandar Kereta Api 26. Electronic Cargo Smart Seal (Jointech) — E-Seal Anti-Tamper
15 PERANGKAT BLUEPRINT (INFRASTRUKTUR FISIK 35 HA)
Utilitas Jaringan, Kelistrikan, Daya Cadangan & Keselamatan
3. CCTV Yard 4 MP (Hikvision) — 32 Titik Tiang Penumpukan 4. CCTV Yard 8 MP 4K ColorVu — 16 Titik Pagar Perimeter 5. CCTV PTZ 360° TandemVu — 8 Titik Menara Pengawas Pusat 8. RFID Tag Pasif UHF ISO — 500 Tag Ditempel di Kaca Truk 9. Automatic Barrier Gate — 4 Unit Palang Gerbang Masuk/Keluar 11. Industrial Switch PoE+ IP40 — 12 Junction Box Lapangan 12. Access Point WiFi 7 Outdoor (Ubiquiti) — 18 Tiang Yard & Rel 13. Server NVR 64-Ch & Database (Hikvision) — Datacenter 14. Online UPS 5000VA Rackmount (APC) — Daya Darurat 4.5 kW 15. Barcode / QR Scanner Meja (Zebra) — 8 Unit Loket Pos 16. Thermal Camera Reefer Yard — 4 Unit Pencegah Kebakaran 17. GPS Tracker Truk 4G (Teltonika) — 40 Unit Armada Jalan Raya 19. Gantry Container X-Ray 6 MeV (Nuctech) — Rp 12,5 Miliar Bea Cukai 20. Vehicle Mounted Terminal (Zebra VC8300) — 6 Kabin Alat Berat 24. Rugged Mobile PDA (Zebra TC57x) — 10 Unit Tallyman Lapangan

## Slide 4
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Klaster 1: Otomasi Gerbang & Rantai Trigger (28 Detik Selesai)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 4 of 15
TAHAP 1: ANPR
Induction Loop
Massa logam truk melindas loop -> Kamera ANPR capture plat B 9812 UIK via TCP/IP.
TAHAP 2: OCR ISO
Portal Photocell
Peti kemas memotong sinar -> Portal OCR membaca nomor TCKU 8291042 (40HC).
TAHAP 3: TIMBANGAN
Load Cell 80t
Truk berhenti di jembatan timbang -> Indikator kirim berat 32.450 kg via RS-232.
TAHAP 4: EDGE AI PC
Advantech ARK-3532
Validasi lokal tiket & berat SOLAS VGM -> picu relay DC 24V buka palang & kirim JSON.
TAHAP 5: PALANG & LED
Barrier & LED
LED tampilkan 'MENUJU BLOK B04' -> Palang terbuka -> Webhook Odoo terbit Rp 50.000.

## Slide 5
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Klaster 2: Telemetri Alat Berat & Penumpukan 3D Presisi Tinggi
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 5 of 15
SPREADER TWISTLOCK KIT (#22)
Deteksi Penguncian Fisik
• Model: Bromma SmartSpreader Kit • Pemicu: Pin hidrolik berputar 90° dalam corner casting peti kemas. • Sensor: Proximity sensor mendeteksi logam pin (LOCKED / UNLOCKED). • Load Cell: Mengukur tonase angkat riil saat boom bergerak. • Aksi Odoo: Transisi ke UNLOCKED memicu tagihan Jasa Lift-Off Rp 250.000!
DGPS / RTK GNSS RECEIVER (#21)
Akurasi Sentimeter (< 2 cm)
• Model: CHCNAV CGI-610 Dual-Antenna • Pemicu: Sinyal satelit + koreksi diferensial base station lokal + IMU boom. • Drop Trigger: Saat twistlock terbuka, koordinat spatio-temporal (X,Y,Z) dikunci detik itu juga. • YMS: Mengonversi koordinat ke format Block B, Bay 04, Row 02, Tier 03. • Meniadakan kesalahan salah letak kontainer!
VMT KABIN & MOBILE PDA (#20 & #24)
Komputer Lapangan (Blueprint)
• Model: Zebra VC8300 (VMT) & Zebra TC57x (PDA) • Layar ultra-bright 8 inci & scanner 2D tahan banting IP66/IP68. • Menampilkan job dispatching antrean pemindahan kontainer ke operator crane. • PDA digunakan tallyman untuk inspeksi fisik bodi kontainer (EIR - Equipment Interchange Receipt).

## Slide 6
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Klaster 3, 4, & 5: Cold Chain Reefer, Rel Kereta Api, & Pabean
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 6 of 15
SMART REEFER SOCKET (#23)
Cold Chain 300 Titik
• Model: Marechal 380V/32A Decontactor • Pemicu: Steker dicolok -> Trafo arus (CT) mendeteksi arus start > 5A. • Proteksi: Jika arus drop mendadak ke 0A (kompresor mati), alarm trip menyala dalam 3 detik. • Aksi Odoo: Setiap shift (8 jam), terbit tagihan Jasa Steker Reefer Rp 250.000 / shift.
RAIL AXLE COUNTER (#25)
Intermodal Rail Siding
• Model: Frauscher RSR123 (SIL 4, IP68) • Pemicu: Pelek roda baja KA memotong medan induktif di leher rel sepur simpan. • Logika: Mencacah as roda (120 as = 30 gerbong datar = 60 TEUs). • YMS: Ubah status rel menjadi OCCUPIED. • Aksi Odoo: Validasi sewa rel (Track Access Charge) ke PT KAI Logistik.
SMART E-SEAL GPS (#26)
Integritas Bea Cukai
• Model: Jointech JT701 GPS Smart Lock • Pemicu: Kawat baja dikunci di Priok -> GPS aktifkan status SEAL_ARMED. • Tamper Alert: Jika kawat dipotong paksa di jalan, alarm sabotase dikirim via 4G. • Aksi Odoo: Wajib berstatus SPPB Cleared sebelum modul Odoo Inventory mengizinkan rilis Delivery Order (DO).

## Slide 7
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Matriks Integrasi Data: Hardware ➔ YMS ➔ ERP Odoo
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 7 of 15
Hardware | Kategori | Protokol | Aksi di YMS | Modul ERP Odoo | Dampak Finansial
Kamera ANPR (#1) | Simulasi | TCP/IP HTTP Post | Validasi plat truk di DB | Odoo Fleet | Rekonsiliasi Armada
Kamera OCR ISO (#2) | Simulasi | Ethernet Socket | Identifikasi nomor box 40HC | Odoo Sales | Penetapan Tarif 40ft
Timbangan 80t (#6) | Simulasi | Serial RS-232 | Validasi SOLAS VGM (<34t) | Odoo Invoicing | Tagihan Timbang Rp 50rb
RFID Reader (#7) | Simulasi | Wiegand / TCP | Identifikasi e-Pass supir | Odoo Accounting | Potong Deposit Supir
Edge AI PC (#18) | Simulasi | REST API JSON | Gateway keputusan gerbang | Odoo API Gateway | Pengirim Webhook Event
DGPS RTK (<2cm) (#21) | Simulasi | NMEA-0183 Serial | Auto-update Bay-Row-Tier | Odoo Maintenance | Jam Jalan Alat Berat
Twistlock Spreader (#22) | Simulasi | CANopen / Proximity | Konfirmasi box dilepas di yard | Odoo Invoicing | Tagihan Lo-Lo Rp 250rb
Smart Reefer (#23) | Simulasi | Modbus / LoRaWAN | Monitoring suhu & trip listrik | Odoo Invoicing | Tagihan Steker Rp 250rb
Axle Counter (#25) | Simulasi | Pulsa / Modbus TCP | Hitung gerbong & okupansi rel | Odoo Purchase | Validasi Sewa Rel (TAC)
15 Item Blueprint Lain | Blueprint | FO, NVR, UPS, CCTV | Utilitas fisik & keamanan 35Ha | Odoo Asset | Depresiasi Aset Tetap

## Slide 8
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Bukti Uji Postman: Struktur Payload JSON Riil
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 8 of 15
POSTMAN REQUEST: TRIGGER GATE-IN & VGM SCALE
POST /api/simulator_action.php?action=gate_in Content-Type: application/json { "device_source": "ADVANTECH_EDGE_PC_GATE_01", "sensor_telemetry": { "anpr_license_plate": "B 9812 UIK", "ocr_container_number": "TCKU8291042", "ocr_iso_code": "42G1", "container_size": "40FT_HIGH_CUBE", "rfid_driver_tag": "RFID-TRK-9812", "measured_gross_kg": 32450, "truck_tare_kg": 11200, "vgm_net_kg": 21250, "vgm_solas_status": "VERIFIED_PASS" } }
WEBHOOK OUTPUT: YMS ➔ ERP ODOO INVOICING
POST https://erp.cidp.ac.id/api/v1/billing/charge-event Authorization: Bearer SECRET_TOKEN_CIDP_2026 { "event_id": "EVT-20260923-0042", "customer_id": "CUST-SAMUDERA-01", "customer_name": "PT Samudera Logistik Prima", "container_number": "TCKU8291042", "billing_breakdown": [ { "service_code": "SRV-VGM", "description": "Jembatan Timbang VGM 80t", "amount": 50000 }, { "service_code": "SRV-LIFT-OFF", "description": "Jasa Lift-Off Peti Kemas 40ft", "amount": 250000 } ], "total_billable_idr": 300000, "status": "AUTO_INVOICE_GENERATED" }

## Slide 9
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Rekapitulasi Rencana Anggaran Belanja Modal (CAPEX Rp 18,94 Miliar)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 9 of 15
No | Klaster Operasional | Jumlah Item | Total Unit | Subtotal CAPEX | Persentase
1 | Otomasi Gate & Kontrol Akses | 8 Jenis | 522 Unit / Pack | Rp 1.460.500.000 | 7.7%
2 | Telemetri Lapangan Penumpukan & Crane | 4 Jenis | 28 Unit | Rp 1.084.000.000 | 5.7%
3 | Cold Chain & Monitoring Reefer Yard | 2 Jenis | 304 Unit / Titik | Rp 2.670.000.000 | 14.1%
4 | Infrastruktur Intermodal Rel KA | 3 Jenis | 62 Unit | Rp 569.600.000 | 3.0%
5 | Keamanan Terminal & Bea Cukai (X-Ray) | 5 Jenis | 157 Unit / Sistem | Rp 13.118.400.000 | 69.3%
6 | Core Datacenter, Edge PC & Jaringan | 4 Jenis | 26 Unit | Rp 660.800.000 | 3.5%
TOTAL | Seluruh Fasilitas CIDP 35 Hektar | 26 Item | 1.099 Unit | Rp 18.943.300.000 | 100.0%

## Slide 10
TOPIK 7: INLAND CONTAINER DEPOT (ICD) & DRY PORT MANAGEMENT
Kesimpulan: Efisiensi Operasional & Akuntabilitas Finansial
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 10 of 15
AKURASI PENEMPATAN 100%
Meniadakan Kesalahan Salah Letak Kontainer
Kombinasi dual-antenna DGPS RTK (< 2 cm) dan proximity sensor twistlock memastikan koordinat 3D Bay-Row-Tier ter-update secara otomatis tanpa input radio manual.
WAKTU TRANSAKSI GATE 28 DETIK
Mengeliminasi Kemacetan Antrean Truk
Otomasi paralel kamera ANPR, OCR portal, jembatan timbang 80t, dan pembaca e-Pass RFID UHF memangkas waktu proses gerbang hingga 37% dibanding sistem manual.
ZERO REVENUE LEAKAGE
Nol Kebocoran Pendapatan Jasa Terminal
Setiap aktivitas fisik alat di lapangan seketika menjadi bukti transaksi sah yang menembakkan tagihan otomatis ke modul ERP Odoo Invoicing tanpa campur tangan staf admin.
KESIAPAN ARSITEKTUR PLUG-AND-PLAY
Teruji Sepenuhnya Menggunakan Postman JSON
Pemisahan sistem 3-layer menjamin bahwa hardware fisik di lapangan kelak tinggal mengarahkan pengiriman data ke endpoint API yang sama tanpa mengubah kode software.

## Slide 11
LAMPIRAN A: DOKUMENTASI RESMI PERANGKAT
Lampiran Visual: Perangkat Simulasi Live Software (Bagian 1)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 11 of 15
ITEM #18: INDUSTRIAL EDGE AI PC
Advantech ARK-3532 Fanless
Intel Core i7, Fanless -20°C s/d 60°C, 4x COM RS-232/422/485, Dual GbE PoE. Pengirim utama JSON ke YMS & Odoo.
ITEM #21: DGPS / RTK GNSS RECEIVER
CHCNAV CGI-610 Dual-Antenna
Akurasi RTK < 2 cm, 50 Hz, IMU sensor, IP67. Terpasang pada boom Reach Stacker untuk auto Bay-Row-Tier.
ITEM #22: SPREADER TWISTLOCK KIT
Bromma SmartSpreader Kit
4x Proximity sensor + 4x load cell, CANopen. Deteksi status LOCKED/UNLOCKED pemicu tagihan Lo-Lo Rp 250rb.

## Slide 12
LAMPIRAN A: DOKUMENTASI RESMI PERANGKAT
Lampiran Visual: Perangkat Simulasi Live Software (Bagian 2)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 12 of 15
ITEM #23: SMART REEFER SOCKET
Marechal 380V/32A Receptacle
Daya 380V/32A IP67, energy meter kWh digital, Modbus/LoRaWAN, trip alarm. Pemicu tagihan plugging Rp 250rb/shift.
ITEM #25: RAIL AXLE COUNTER
Frauscher RSR123 Wheel Sensor
Sensor induktif pelek roda KA, SIL 4, IP68. Menghitung gerbong kontainer & okupansi sepur rel intermodal.
ITEM #26: SMART E-SEAL GPS
Jointech JT701 GPS Smart Lock
Gembok elektronik GPS/GSM/RFID, sensor kabel anti-potong. Integritas pabean Priok-CIDP (syarat DO Odoo).

## Slide 13
LAMPIRAN B: DOKUMENTASI RESMI PERANGKAT
Lampiran Visual: Perangkat Blueprint Fasilitas Fisik
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 13 of 15
ITEM #24: RUGGED MOBILE PDA
Zebra TC57x / Honeywell CT60
Android Enterprise, 2D Barcode Imager, IP68 tahan air & jatuh 1.8m. Digunakan petugas tallyman untuk pembuatan bukti serah terima kontainer (EIR).
REFERENSI KATALOG RESMI 14 PERANGKAT BLUEPRINT LAINNYA
• Item #3: CCTV Yard 4 MP (Hikvision DS-2CD2046G2H-IU) — 32 Unit Tiang Tumpukan • Item #4: CCTV Yard 8 MP 4K ColorVu (Hikvision DS-2CD2T87G2H-LI) — 16 Unit Pagar Perimeter • Item #5: CCTV PTZ 360° TandemVu (Hikvision DS-2SE4C425MWG) — 8 Unit Menara Pengawas • Item #8: RFID Tag Pasif UHF ISO 18000-6C — 500 Tag Ditempel di Kaca Truk Mitra • Item #9: High-Speed Automatic Barrier Gate — 4 Unit Palang Gerbang Buka 1.2 Detik • Item #11: Industrial Switch PoE+ Managed IP40 — 12 Unit Junction Box Lapangan • Item #12: Outdoor Access Point WiFi 7 (Ubiquiti U7 Pro) — 18 Tiang Yard & Rel KA • Item #13: Server NVR 64-Ch & Database (Hikvision DS-9664NI-M16/R) — Datacenter • Item #14: Online UPS 5000VA Rackmount (APC SRT5KRMXLI) — Daya Darurat 4.5 kW • Item #15: Barcode / QR Scanner Meja (Zebra Symbol LS2208) — 8 Unit Loket Pos • Item #16: Thermal Camera Reefer Yard (Hikvision DS-2TD2636B) — 4 Unit Anti Kebakaran • Item #17: GPS Tracker Truk 4G (Teltonika TAT240) — 40 Unit Armada Koridor Priok-CIDP • Item #19: Gantry Container X-Ray Scanner 6 MeV (Nuctech MB1215DE) — Rp 12,5 Miliar • Item #20: Vehicle Mounted Terminal (Zebra VC8300 Rugged 8") — 6 Kabin Crane

## Slide 14
LAMPIRAN C: MASTER BILL OF MATERIALS (BOM)
Tabel Lengkap 26 Hardware & Spesifikasi (Item #1 s/d #13)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 14 of 15
No | Nama Hardware | Model / Tipe Rekomendasi | Klasifikasi | Harga Satuan | Subtotal CAPEX
1 | Kamera ANPR Gate | Hikvision DS-TCG406-E Series | Simulasi | Rp 16.000.000 | Rp 64.000.000 (4 unit)
2 | Kamera OCR Kontainer | Hikvision iDS-TCV300-A6I | Simulasi | Rp 55.000.000 | Rp 220.000.000 (4 unit)
3 | CCTV Yard 4 MP | Hikvision DS-2CD2046G2H-IU | Blueprint | Rp 3.500.000 | Rp 112.000.000 (32 unit)
4 | CCTV Yard 8 MP 4K | Hikvision DS-2CD2T87G2H-LI | Blueprint | Rp 6.500.000 | Rp 104.000.000 (16 unit)
5 | CCTV PTZ 360° | Hikvision DS-2SE4C425MWG | Blueprint | Rp 10.300.000 | Rp 82.400.000 (8 unit)
6 | Weighbridge 80 Ton | Fangda Electronic Truck Scale | Simulasi | Rp 267.000.000 | Rp 534.000.000 (2 unit)
7 | RFID Reader UHF 20m | Long-Range UHF Reader 20m | Simulasi | Rp 3.000.000 | Rp 12.000.000 (4 unit)
8 | RFID Tag UHF ISO | UHF Anti-Metal ISO 18000-6C | Blueprint | Rp 690.000 / pack | Rp 34.500.000 (50 pack)
9 | Automatic Barrier Gate | High-Speed DC Brushless Gate | Blueprint | Rp 60.000.000 | Rp 240.000.000 (4 unit)
10 | LED Info Display | Chipshow Outdoor P6/P8 LED | Simulasi | Rp 47.000.000 | Rp 188.000.000 (4 unit)
11 | Industrial Switch PoE+ | Managed 24-Port GbE IP40 | Blueprint | Rp 10.000.000 | Rp 120.000.000 (12 unit)
12 | Outdoor Access Point | Ubiquiti U7 Pro WiFi 7 | Blueprint | Rp 7.200.000 | Rp 129.600.000 (18 unit)
13 | Server NVR & DB Core | Hikvision DS-9664NI-M16/R | Blueprint | Rp 102.000.000 | Rp 204.000.000 (2 unit)

## Slide 15
LAMPIRAN C: MASTER BILL OF MATERIALS (BOM)
Tabel Lengkap 26 Hardware & Spesifikasi (Item #14 s/d #26)
Armansyah Muchtarrom — Hardware Specialist | Topik 7: ICD & Dry Port Management (CIDP 35 Ha) Slide 15 of 15
No | Nama Hardware | Model / Tipe Rekomendasi | Klasifikasi | Harga Satuan | Subtotal CAPEX
14 | Online UPS 5000VA | APC Smart-UPS SRT5KRMXLI | Blueprint | Rp 81.000.000 | Rp 324.000.000 (4 unit)
15 | Barcode / QR Scanner | Zebra Symbol LS2208 USB | Blueprint | Rp 1.600.000 | Rp 12.800.000 (8 unit)
16 | Thermal Camera Reefer | Hikvision DS-2TD2636B-13/P | Blueprint | Rp 30.000.000 | Rp 120.000.000 (4 unit)
17 | GPS Tracker Truk 4G | Teltonika TAT240 4G LTE | Blueprint | Rp 2.500.000 | Rp 100.000.000 (40 unit)
18 | Industrial Edge AI PC | Advantech ARK-3532 Fanless | Simulasi | Rp 42.000.000 | Rp 168.000.000 (4 unit)
19 | Gantry X-Ray Scanner | Nuctech MB1215DE 6 MeV | Blueprint | Rp 12.500.000.000 | Rp 12.500.000.000 (1 set)
20 | VMT Kabin Alat Berat | Zebra VC8300 Rugged 8" | Blueprint | Rp 74.000.000 | Rp 444.000.000 (6 unit)
21 | DGPS / RTK Receiver | CHCNAV CGI-610 GNSS/INS | Simulasi | Rp 45.000.000 | Rp 270.000.000 (6 unit)
22 | Spreader Twistlock Kit | Bromma SmartSpreader Kit | Simulasi | Rp 35.000.000 | Rp 210.000.000 (6 unit)
23 | Smart Reefer Socket | Marechal 380V/32A Receptacle | Simulasi | Rp 8.500.000 | Rp 2.550.000.000 (300 unit)
24 | Rugged Mobile PDA | Zebra TC57x Handheld IP68 | Blueprint | Rp 16.000.000 | Rp 160.000.000 (10 unit)
25 | Rail Axle Counter | Frauscher RSR123 Wheel Sensor | Simulasi | Rp 85.000.000 | Rp 340.000.000 (4 sensor)
26 | Smart E-Seal GPS | Jointech JT701 GPS Smart Lock | Simulasi | Rp 3.200.000 | Rp 320.000.000 (100 unit)